# Comprehensive CAD Vocabulary & Mechanical Engineering Terminology Guide
Mike, this is a great foundation to build — knowing the precise terminology is the difference between getting garbage out of a CAD-generating LLM and getting something manufacturable. Let me break this down systematically.

## 1. Fundamental CAD Operations (The Verbs)
These are the actions you perform on geometry. Every parametric CAD system (SolidWorks, FreeCAD, Fusion 360, OnShape) uses these concepts.
Sketch-Level Operations
- Sketch — A 2D drawing on a plane or face that defines the cross-sectional profile of a 3D feature. Everything starts here.
- Constraint — Geometric rules applied to sketch entities (horizontal, vertical, coincident, tangent, concentric, equal, symmetric). A fully constrained sketch has zero degrees of freedom.
- Construction Geometry — Reference lines/circles used to position other geometry but not included in the final profile. Also called reference geometry.
- Spline — A smooth freeform curve defined by control points. B-splines and NURBS (Non-Uniform Rational B-Splines) are the mathematical backbone of all modern CAD surfaces.
- Offset — Creating a curve parallel to an existing edge at a specified distance.
- Trim / Extend — Cutting a sketch entity at an intersection or lengthening it to meet another entity.
3D Feature Operations (Sketch-Based)
- Extrude (Boss/Cut) — Pulling a 2D sketch linearly along an axis to create a solid (boss) or remove material (cut). The single most common operation.
- Revolve — Rotating a 2D profile around an axis to create axially symmetric bodies (shafts, bottles, bowls, nozzles).
- Sweep — Moving a 2D profile along a 3D path (pipes, cables, helical features, handrails).
- Loft — Blending between two or more 2D profiles at different positions to create a smooth transitional shape (aerodynamic fairings, bottle transitions, turbine blades).
- Pad — Same as extrude in some CAD systems (FreeCAD uses "Pad" and "Pocket").
- Pocket — A cut extrusion in FreeCAD terminology.
3D Feature Operations (Applied)
- Fillet — Rounding an edge with a specified radius. Can be constant, variable, or face-blended.
- Chamfer — Cutting an edge at an angle, creating a flat bevel. Defined by distance × distance or distance × angle.
- Shell — Hollowing out a solid body to a specified wall thickness, optionally removing one or more faces (creating open containers, enclosures).
- Draft — Applying a taper angle to faces, critical for injection molding so parts release from molds.
- Rib — A thin wall feature connecting a boss to a wall for structural reinforcement.
- Pattern — Duplicating features in linear arrays, circular arrays, or driven by a curve/sketch. Includes linear pattern, circular pattern, and mirror.
- Boolean Operations — Union (add), Subtract (cut), Intersect (keep only overlap) between solid bodies.
- Hole Wizard — Parametric creation of standard holes: counterbored, countersunk, tapped, through, blind.

## 2. Mechanical Components & Feature Terminology (The Nouns)
### Fastener & Thread Features
- Thread — A helical ridge on a cylindrical surface for fastening or motion. Defined by pitch (distance between threads), major diameter, minor diameter, and thread form (profile shape).
  - External thread — On a shaft/bolt (male).
  - Internal thread — Inside a hole/nut (female).
  - Thread standards: Metric (M8×1.25 = 8mm major dia, 1.25mm pitch), UNC/UNF (Unified National Coarse/Fine), ACME (trapezoidal, for power transmission), Buttress (asymmetric, for unidirectional loads).
- Tap / Tapped Hole — A hole with internal threads cut into it.
- Counterbore (CBORE) — A flat-bottomed cylindrical recess that allows a bolt head to sit flush or below surface.
- Countersink (CSK) — A conical recess for flat-head screws to sit flush.
- Spotface — A shallow counterbore to create a flat seating surface on a rough casting.
- Clearance Hole — A hole slightly larger than the fastener, allowing it to pass through without threading.
- Press Fit / Interference Fit Hole — A hole slightly smaller than the inserted component, creating a friction-based joint.
- Helicoil / Thread Insert — A coiled wire insert for reinforcing threads in soft materials (aluminum, plastic).
### Shaft & Rotational Features
- Shaft — A cylindrical component designed to transmit torque and rotation.
- Keyway / Key Seat — A rectangular slot cut into a shaft and mating hub to transmit torque via a key (a rectangular bar).
- Spline (mechanical) — Multiple ridges along a shaft that engage with grooves in a mating part. Higher torque capacity than a single key. Not to be confused with the CAD curve type.
- Knurl — A textured pattern (diamond or straight) rolled onto a cylindrical surface for grip or press-fit retention.
- Journal — The portion of a shaft that sits inside a bearing.
- Shoulder / Step — A diameter change along a shaft that provides axial location for bearings, gears, or other components.
- Undercut / Relief Groove — A narrow groove cut at a diameter transition to allow full thread engagement or grinding wheel clearance.
- Center Hole — A conical hole in the end of a shaft for lathe center support during machining.
### Flange & Connection Features
- Flange — A protruding rim or collar used for strengthening, attachment, or sealing. Types include:
  - Weld Neck Flange — Has a long tapered hub, welded to pipe. Highest integrity.
  - Slip-On Flange — Slides over pipe and is fillet welded. Easier to align.
  - Blind Flange — A solid plate that caps off a pipe end.
  - Lap Joint Flange — Used with a stub end, allowing rotation for bolt alignment.
  - Threaded Flange — Screws onto a threaded pipe end.
  - Socket Weld Flange — Pipe inserts into a socket and is fillet welded.
- Bolt Circle Diameter (BCD) — The diameter of the imaginary circle passing through the center of bolt holes on a flange.
- Gasket Seat / Raised Face — The machined surface on a flange face where a gasket sits to create a seal.
- Boss — A raised cylindrical feature on a surface, typically for mounting fasteners or aligning components (very common in injection-molded plastic parts).
- Lug — A protruding bracket or ear used as an attachment or lifting point.
- Gusset — A triangular plate or rib used to reinforce a joint between two surfaces.
### Hole & Cavity Features
- Blind Hole — A hole that does not pass completely through the material. Has a defined depth.
- Through Hole — A hole that passes completely through.
- Bore — A precision cylindrical hole, often machined to tight tolerances for bearing or shaft fitment.
- Recess / Pocket — A shallow cavity machined into a surface.
- Slot — An elongated hole or groove (T-slot, dovetail slot, keyway slot).
- Groove — A channel cut into a surface. O-ring groove is a specific type sized to ASTM/ISO standards for elastomeric seal retention.
- Datum — A reference feature (plane, axis, or point) from which dimensions and tolerances are measured.
### Bearing & Motion Features
- Bearing Seat — A precision bore or shaft surface where a bearing mounts. Tolerance class determines fit type.
- Bushing — A cylindrical sleeve that acts as a plain bearing or adapter between two different diameters.
- Retaining Ring Groove (Snap Ring Groove) — A narrow circumferential groove for a circlip/snap ring that axially retains a component on a shaft or in a bore.
- Cam — A rotating or sliding piece that converts rotary motion to linear motion via a shaped profile (lobe).
- Detent — A spring-loaded ball or pin that drops into a notch to hold a mechanism in a defined position.
- Clevis — A U-shaped bracket with a pin hole, used for pin-joint connections (linkages, hydraulic cylinders).
- Trunnion — A cylindrical pivot or mounting pin, often integral to a component (hydraulic cylinders, cannons).
### Sheet Metal Features
- Bend — A formed angle in sheet metal defined by bend radius, bend angle, and bend allowance (material stretch compensation).
- K-Factor — The ratio of the neutral axis location to material thickness, governing bend allowance calculation.
- Hem — A fold where sheet metal is bent back onto itself (open hem, closed hem, teardrop hem) for edge stiffness and safety.
- Tab — A protruding feature formed by cutting three sides and bending.
- Louver — A lance-and-form feature creating a slotted ventilation opening.
- Dimple / Lance — A small formed protrusion or partially cut-and-bent feature.
- Flat Pattern — The unfolded/developed 2D layout of a sheet metal part before bending. Critical for laser cutting and CNC punching.
- Jog / Offset Bend — Two bends creating a step/offset in the sheet.
- Bead — A formed ridge for stiffening a flat panel.
- Emboss / Deboss — Raised or recessed formed features in sheet metal (logos, stiffeners, locators).
### Seal & Gasket Features
- O-Ring Gland — A precisely dimensioned groove (axial or radial) sized per AS568 or ISO 3601 standards to compress an O-ring for sealing.
- Face Seal — Sealing between two flat surfaces (gasket type).
- Radial Seal — Sealing between a shaft and bore (lip seal, O-ring in radial gland).
- Labyrinth Seal — A non-contact seal using tortuous paths to restrict fluid flow (turbomachinery).
### Gear Terminology
- Spur Gear — Straight-tooth gear for parallel shaft power transmission.
- Helical Gear — Angled teeth, smoother and quieter than spur, generates axial thrust.
- Bevel Gear — Conical gears for intersecting shafts (typically 90°).
- Worm Gear — A screw (worm) meshing with a wheel, high reduction ratio, self-locking capability.
- Rack and Pinion — Converts rotary to linear motion (steering systems).
- Module (m) — Metric gear sizing: m = pitch diameter / number of teeth. (Diametral Pitch is the imperial equivalent.)
- Pitch Circle — The imaginary circle where gear teeth effectively mesh.
- Addendum — Tooth height above the pitch circle.
- Dedendum — Tooth depth below the pitch circle.
- Involute Profile — The standard tooth curve shape that maintains constant velocity ratio.
- Backlash — The clearance between mating gear teeth.
- Root Fillet — The radius at the base of a gear tooth (stress concentration area).
### Structural / Weldment Features
- Structural Member / Profile — Extruded cross-sections: I-beam, C-channel, L-angle, T-section, HSS (Hollow Structural Section — square/rectangular tube), round tube.
- Weld Bead — The deposited material joining two components. CAD represents this as cosmetic or structural features.
- Weld Symbols — Standardized annotations (AWS A2.4) indicating joint type, weld type (fillet, groove, plug, slot, seam), size, and finishing.
- Miter Joint — Members meeting at an angle, each cut to half the included angle.
- Cope — A profile cut into the end of one structural member to fit against another's shape.
- End Cap — A plate closing the open end of a hollow structural section.

## 3. Assembly & Relationship Terminology
- Mate / Constraint — Defining spatial relationships between components: coincident, concentric, parallel, perpendicular, tangent, distance, angle, gear, cam, rack-pinion.
- Degrees of Freedom (DOF) — The remaining unconstrained motions. A fully constrained component has 0 DOF. A hinge has 1 DOF (rotation about one axis).
- Sub-Assembly — A group of parts assembled together that functions as a unit within a larger assembly.
- BOM (Bill of Materials) — The structured list of all components, quantities, materials, and part numbers in an assembly.
- Interference Check / Clash Detection — Automated verification that no two solid bodies occupy the same space.
- Exploded View — Components separated along assembly vectors to show relationships and assembly sequence.
- Tolerance Stack-Up — The cumulative effect of individual part tolerances on assembly fit and function. Critical for multi-part assemblies.

## 4. Tolerancing & Dimensioning (GD&T)
GD&T — Geometric Dimensioning and Tolerancing (ASME Y14.5 / ISO 1101) is the universal language for defining allowable variation. CAD-generating LLMs that produce manufacturing drawings need these terms.
- Feature Control Frame — The rectangular box containing the geometric tolerance symbol, tolerance value, and datum references.
- Flatness — How much a surface can deviate from a perfect plane.
- Straightness — How much a line element can deviate from perfectly straight.
- Circularity (Roundness) — How much a cross-section deviates from a perfect circle.
- Cylindricity — Combines circularity, straightness, and taper over the full length of a cylinder.
- Perpendicularity — How much a feature deviates from 90° to a datum.
- Parallelism — How much a feature deviates from being parallel to a datum.
- Angularity — How much a feature deviates from a specified angle to a datum.
- Position (True Position) — How much a feature's actual center can deviate from its theoretically exact location.
- Concentricity — How much the median points of a feature deviate from a datum axis.
- Runout (Circular / Total) — Variation measured when a part is rotated about a datum axis. Controls wobble.
- Profile (Line / Surface) — Controls the shape of a 2D line or 3D surface relative to a theoretical profile.
- Maximum Material Condition (MMC) — The state where a feature contains the most material (largest shaft, smallest hole).
- Least Material Condition (LMC) — The opposite — least material (smallest shaft, largest hole).
- Regardless of Feature Size (RFS) — Tolerance applies independent of actual size.

## 5. Surface Finish & Material Specifications
- Surface Roughness (Ra) — Arithmetic average of surface deviations from the mean, measured in micrometers (μm) or microinches (μin). Ra 0.8 μm = fine machined. Ra 3.2 μm = standard machined. Ra 12.5 μm = rough.
- Surface Finish Symbols — Indicate required roughness, lay direction, machining allowance, and process on drawings.
- Hardness Callouts — HRC (Rockwell C), HRB, HV (Vickers), HB (Brinell) — specified in material or surface treatment notes.
- Heat Treatment — Case hardening, through hardening, annealing, tempering, nitriding, carburizing.
- Surface Treatment — Anodizing (aluminum), zinc plating, powder coating, electroless nickel, chrome plating, passivation (stainless steel), black oxide.

## 6. Manufacturing Process Awareness for CAD
Understanding these informs what geometry is manufacturable:
- CNC Milling — Tool radius dictates minimum internal corner radius. Deep narrow pockets are expensive. Prefer standard tool sizes.
- CNC Turning/Lathe — For axially symmetric parts. Internal features limited by boring bar reach.
- Injection Molding — Requires draft angles (1-3°), uniform wall thickness, radiused corners, and consideration of parting lines, gate locations, and ejector pin marks.
- 3D Printing / Additive Manufacturing — Minimum wall thickness, overhang angles (typically >45° from horizontal needs support), layer resolution limitations.
- Sheet Metal Fabrication — Minimum bend radius (typically ≥ material thickness), minimum flange length, punch-to-bend clearance, grain direction considerations.
- Casting — Draft angles, minimum wall thickness, fillet all internal corners, avoid sharp section changes (causes hot spots/porosity).
- Welding — Joint accessibility, distortion management, weld symbol specification, material weldability.

## 7. Free & Open-Source Study Resources
### CAD Software (Free)
- FreeCAD (freecad.org) — Fully open-source parametric CAD. Part Design, Assembly, Sheet Metal, FEM, TechDraw workbenches. Best for learning fundamentals without licensing costs.
- Onshape Free (onshape.dev/signup) — Browser-based, professional-grade parametric CAD. Free tier is public-only. Excellent for learning SolidWorks-style workflows.
- Fusion 360 Personal (autodesk.com) — Free for personal/non-commercial use. Parametric modeling, CAM, simulation, PCB design.
- OpenSCAD (openscad.org) — Code-based/programmatic CAD using a scripting language. Excellent pairing with LLM-generated geometry since it's inherently text-based.
- Blender (blender.org) — Primarily mesh/surface modeling but has CAD-oriented addons. Better for organic shapes and visualization than precision engineering.
- LibreCAD (librecad.org) — Open-source 2D CAD for drafting (AutoCAD LT equivalent).
- KiCad (kicad.org) — Open-source PCB/electronics CAD if your projects cross into electrical.
### Learning Resources (Free)
- MIT OpenCourseWare 2.007 (ocw.mit.edu) — Design and Manufacturing I. Covers fundamental mechanical design principles.
- MIT OCW 2.008 — Design and Manufacturing II. Production processes.
- MIT OCW 2.003/2.004 — Dynamics and Controls, modeling mechanical systems.
- FreeCAD Wiki & Tutorials (wiki.freecad.org) — Comprehensive documentation with step-by-step tutorials for every workbench.
- MangoJelly Solutions (YouTube) — Widely regarded as the best FreeCAD tutorial series. Methodical, well-paced.
- Lars Christensen (YouTube) — Excellent Fusion 360 tutorials from beginner to advanced.
- Engineers Edge (engineersedge.com) — Free reference for mechanical engineering formulas, thread tables, tolerance charts, GD&T references, material properties.
- Machinery's Handbook — Not free, but the single most essential mechanical engineering reference. The "bible" of the trade. Worth owning.
- ASME Y14.5 GD&T — The standard itself costs money, but numerous free tutorials exist:
  - GD&T Basics (gdandtbasics.com) — Free tutorials covering every symbol and concept.
  - Tec-Ease GD&T Tips (tec-ease.com) — Free tip archive with visual examples.
- McMaster-Carr (mcmaster.com) — Not a learning resource per se, but an invaluable reference. Every product has detailed CAD models, dimensions, and specifications. Browsing their catalog teaches you what standard components exist and how they're specified.
- GrabCAD (grabcad.com) — Free library of CAD models. Study how experienced engineers model complex assemblies.
- TraceParts / 3D ContentCentral — Free standard component libraries (bearings, fasteners, seals, actuators) with downloadable CAD models.
- Textbook: "Shigley's Mechanical Engineering Design" — The standard university textbook. Older editions are widely available. Covers fastener design, shaft design, gear design, bearing selection, fatigue analysis — everything you'd need to understand why these features exist.
- Textbook: "Engineering Drawing and Design" by Madsen — Covers drawing standards, dimensioning, GD&T, and how CAD drawings communicate manufacturing intent. Older editions are affordable.
### Specifically for LLM-Driven CAD Prompting
- OpenSCAD is your strongest candidate for LLM-generated geometry because it's text/code-based. You can prompt an LLM to write OpenSCAD scripts, iterate, and render.
- CadQuery (github.com/CadQuery/cadquery) — Python-based parametric CAD library. Write Python → get STEP/STL files. Extremely well-suited for LLM code generation.
- Build123d (github.com/gumyr/build123d) — Modern Python CAD library, successor philosophy to CadQuery. Clean API, great for programmatic/LLM workflows.
- FreeCAD Python Console — FreeCAD exposes its entire modeling kernel via Python. LLMs can generate FreeCAD Python scripts.
- STEP / IGES / STL / 3MF — Know your file formats. STEP (.stp) is the universal exchange format for solid models. STL is for 3D printing (mesh only, no parametric data). IGES is legacy. 3MF is the modern replacement for STL.

## 8. Recommended Learning Path
1. Install FreeCAD + Onshape Free account. Use FreeCAD for offline parametric learning, Onshape for professional-workflow exposure.
2. Work through MangoJelly's FreeCAD Part Design series on YouTube. Model real parts: a flanged shaft, a gearbox housing, a sheet metal bracket.
3. Study GD&T Basics (gdandtbasics.com) to understand how tolerancing language works.
4. Browse McMaster-Carr obsessively. Pick a component category (bearings, shaft collars, structural framing), study the specifications, download the CAD models, and examine how they're built.
5. Learn CadQuery or Build123d for Python-based CAD. This directly translates to LLM-promptable geometry generation.
6. Practice prompting: Take a real component from McMaster-Carr, describe it in natural language using the vocabulary above, and iterate with an LLM to generate the CadQuery/OpenSCAD code that recreates it.
This vocabulary set covers roughly 90% of what you'll encounter in general mechanical CAD work. The remaining 10% is domain-specific (hydraulics, pneumatics, HVAC, piping, injection mold tooling, etc.) and builds on these fundamentals. Let me know if you want to drill into any specific area — sheet metal, gear design, GD&T, or the programmatic CAD pipeline in particular.